# Use of the mouse with PEGEM2

Using the mouse and its buttons is hopefully quite intuitive. Movement of the mouse moves the hand cursor to any point of interest. As the hand approaches the right side of the screen, so it changes to point in the reverse direction, but the end of the finger remains the action point. The buttons have generic meanings as follows:

Left click -	Down, do it, affirmative

Right click -	Up, undo, deny

As with PEGEM, it is possible to pick up a paper tape and move it about the screen. The hand is shown carrying the tape. Note that due to the irreversibility of some actions on the waste bin, an exclamation mark is shown when a tape is in a hazardous place. The specific mouse button actions with and without a paper tape in hand are tabulated below.

## No Tape in hand

|  | Left | Right |
| --- | --- | --- |
| All lever switches, toggle switches | Switch down | Switch up |
| Rotary switches and rotary knobs | Turn anti-clockwise | Turn clockwise |
| Tape punch run-out button | Run-out | - |
| Tape punch output tape | Tear off tape for naming | - |
| Tape cabinet closed drawer | Open drawer | - |
| Tape cabinet open drawer | Close drawer | Close drawer |
| Tape in an open drawer | Pick up tape, close drawer | Close drawer |
| Teleprinter tear-off lever | Tear off and scrap used paper | - |
| Tape reader with tape loaded | - | Return tape to drawer |

## Tape in hand

| Lever and toggle switches, rotary switches and knobs | Operate the switch as normal | Return tape to drawer and operate the switch |
| --- | --- | --- |
| Tape punch run-out button | Run-out | Return tape to drawer |
| Tape punch output tape | Return tape to drawer and tear off tape for naming | Return tape to drawer |
| Closed drawer | Put tape in drawer | Take tape to naming position |
| Tape reader with no tape | Load tape in reader | Return tape to drawer |
| Tape reader with tape loaded | Return loaded tape to drawer; load this tape | Return both tapes to drawer |
| Waste bin | Drop tape in bin (deletes!) | Take tape to naming position |
| Naming position | Renames the tape | Take tape to waste bin |
| Anywhere else | - | Return tape to drawer |
| Teleprinter tear-off lever | Return tape to drawer and scrap used paper | Return tape to drawer |

Chris Burton   14 December 1999.